# Android Accessory Protocol Bridge
Protocol Specification

Version	Date	Remarks
0.4	10/1/2013	Started using versions
0.5	29/01/2013	Added port status service, responsible for sending eof and close on other ports.
0.6	12/03/2013	Removed lies regarding d-bus method calls

# Introduction & goal
AAP-bridge allows various communications between a android phone and a embedded Linux system over the Android accessory protocol. The prime feature is remote procedure calls to your custom application running on the embedded Linux environment.
The protocol described in this document is designed to enable various other protocols on top of Android accessory protocol and allow concurrent use of those sub-protocols.

# Conventions
- The key words "MUST", "MUST NOT", "REQUIRED", "SHALL", "SHALL NOT", "SHOULD", "SHOULD NOT", "RECOMMENDED", "MAY", and "OPTIONAL" in this document are to be interpreted as described in RFC2119.
- All data formats are in little endian, unless otherwise noted.
- NULL terminators have the value zero and have the size of 1 byte.
- In examples the following color codes apply:
  Multiplexed message (Table 1: Multiplexed message).
  Service control message (Table 3: Port open request message and Table 4: Port open status message).
  Variable sized structures
  All other messages will be black on white.
# Scope & platform
The AAB (Android Accessory Bridge) protocol is designed to run on top of the AAP (Android accessory protocol). This makes a few of assumptions. The most important one is the reliability and flow of the underlying protocol (AAP).
At the moment of writing AAP is based on top of two different protocols:
- Bluetooth: Serial Port Profile
- USB: Bulk transfer endpoints
Both offer the reliability and transfer order. AAB will therefore not contain any layer to guarantee this.
The new features in AAP 2.0 - using accessory as audio device and making HID devices available from the accessory - are not within the scope of this document. They do not use the same data stream as the accessory protocol.

# Messages
AAB defines several different messages which can be exchanged between the Android & Linux system. Most of these are located in the application layer. But the most important one is located at the transport layer. The multiplexed message:

Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Destination port					Length of data
4	32	Data [Variable size, max 4000 bytes]

Table 1: Multiplexed message

The purpose of this layer is to allow different application messages at the same time using time-division multiplexing. It looks a lot like the internet TCP protocol but lacks flow control and checksum. As described in “Scope & platform”, those are already provided by the underlying protocols.

The multiplexed message is the only message located at the transport layer, all other messages defined in this document will be encapsulated within this message.

Illustration 1: The data-link and physical layer are provided by the Android accessory protocol.
Please note that multiple bulk transfer and multiple d-bus communications can happen at the same time.
# Multiplexed data streams
Data is exchanged between android and Linux using a bidirectional data stream.
Multiple sub-protocols (Like Bulk data and D-bus) are multiplexed over this steam using a port mechanism. The Android System will request the Linux accessory for a new service. Accessory will respond positive or negative. In case of a positive response, the accessory will return a port number associated with the desired service.
Requesting these new ports is done by communicating with port 1 (The service spawner). You can open a sub-protocol stream by sending a request to port 1. This port is always open.
These ports MUST always be open:
Port	Name	Direction	Description
0	Port status	Bidirectional	Used report status (EOF and CLOSE) on other ports and cleanup services if there port is closed
1	Service spawner	Bidirectional	Used to spawn services and associated ports
2	Keep-alive	Bidirectional	Will respond to keep-alive messages

Table 2: Always open ports
The other ports SHOULD be open-able by requesting additional services from the service spawner. A service will always have a accociated port. Please note the difference from TCP where the sender can send from a different port then the receiver. This is not the case here. Data send from port 5 will always be received on port 5 on the other machine.
## Service Spawner
The service spawner will starts local services on the Accessory and assigns a port to them so they can be reached from the Android device.
There are two kinds of messages used to communicate with the service spawner on port zero. Open messages and open status messages. All communication is synchronous, When multiple open request are send, the responses will return in the correct order. All Open request MUST be answered by a Port status message.

Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	1 - Destination port					Length of data
4	32	'O' {ASCII constant}					Requested protocol					Arguments length 0-3000
8	64	Arguments [Variable size, depends on requested protocol. There is a upper limit of 3000 bytes]

Table 3: Port open request message
Arguments are additional bytes send from the Android device when opening the steam. They are interpreted depending on the requested protocol. The requested protocol should be a identifier from Table 7: Service identifiers.

Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	1 - Destination port					Length of data
4	32	'S'					Port id					Status field
8	64	Error code

Table 4: Port open status message

Status field in the status message SHOULD be one of the following:
STREAM_OPEN 0x01 //Port id field is the port associated with the new service
STREAM_DENIED 0x02 //Port id field must be ignored

Any unknown status fields must be ignored.

The error code field is not populated by the service spawner. It is populated by any of the higher level protocols. Those protocols may implement error code however they wish.

Any unknown status message is ignored. Every “Open request” from Android will result in a STREAM_OPEN or STREAM_DENIED status message back. Only the android system may issue a “Open request” message to the accessory. The accessory MUST NOT try opening port on the Android device.
## Port status service
The port status service is always located on port 0. This service will receive information about end of file and closes on other ports. This is in contrast to the service spawner who open ports.
Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	0 - Destination port					Length of data
4	32	Target port					Status					Padding – must be zero's

Status field can be any of the following:
STREAM_EOF 0x03
STREAM_CLOSE 0x04

There is a difference between sending a EOF and CLOSE:
EOF : I will no longer send data and consider my output closed.
CLOSE: I will no longer interested in receiving data and consider my input closed.

Once both output and input on a port are closed, a cleanup may occur to free all resources and make the port ready for reuse. This situation can occur in the following ways (but not limited to, as all arrows may be reversed and ordered differently):

android_service --EOF--> accessory_service
android_service --CLOSE--> accessory_service
Cleanup now occurs on both sides.

android_service --EOF--> accessory_service
android_service <--EOF-- accessory_service
Cleanup now occurs on both sides.

android_service --CLOSE--> accessory_service
android_service <--CLOSE-- accessory_service
Cleanup now occurs on both sides.

A cleaned up service may not receive or send data.
## Keep-alive
The keep-alive is a mechanism to detect if one of the two parties crashed. This is done by repeatedly sending a ping and waiting for a reply.
Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	2 - Destination port					4 - Length of data
4	32	'P'					'i'					'n'					'g'

Table 5: Ping message

Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	2 - Destination port					4 - Length of data
4	32	'P'					'o'					'n'					'g'

Table 6: Pong reply message
The Ping message SHOULD only be send from Android. The Pong message MUST only be send in response to a Ping message. The Ping frequency may be decided by the Android device, but MUST be within 5 seconds. The accessory MUST close all ports (except the always open ports) if no Ping is received for 6 seconds. The Android device should close all ports in the same way if no Pong message is received within 1 second.
# Supported services
Sub-protocol	Identifier
Bulk data	1
D-Bus function calls	2
D-Bus signal	3

Table 7: Service identifiers
These identifiers are used in “Open stream” messages to the service spawner.
## Bulk data
< To be defined >
## D-bus
Some part of the AAB protocol uses the d-bus marshaled message format. This is used for method returns and d-bus signals. You can read more about this message format on the d-bus specification page.
### D-bus function calls
There are two kind of messages related to remote method invocation. D-bus RPC messages are send from Android to the accessory. For every RPC, a response is send back. This response MUST always be send. The response is a binary d-bus message.
Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Destination port					Length of data
4	32	Padding, MUST be ignored					Arguments size
8	64	Arguments for d-bus methods [Variable sized elements, see Table 9: Arguments for d-bus methods]

Table 8: D-bus RPC message
Field	Specification
Busname	NULL terminated, a empty string is allowed
Object path	NULL terminated, a empty string is allowed
Interface	NULL terminated, a empty string is allowed
FunctionName	NULL terminated, a empty string is allowed
Arguments	A number of arguments. This is a optional field. A argument consist of a ASCII char (describing the type) and a variable size data-type depending on the ASCII char. See Table 10: Argument types for types and sizes. Zero arguments are allowed, in this case this field would be zero bytes.

Table 9: Arguments for d-bus methods
The maximum total size of all arguments combined is 3000 bytes. The Android device MUST NOT send any bigger RPC messages.
The arguments are a sequence of tuples containing a d-bus data type (as a ASCII character) and a byte array (who's size depends on the d-bus type). The field Arguments size lists the amount of arguments, not the amount of bytes. The d-bus type and byte length relation can be read in the following table (No padding is present between the arguments):
Native types		AAB arguments protocol format
D-bus type	Java type	ASCII char	Length of in bytes
BYTE	java.lang.Byte	'y'	1
BOOLEAN	java.lang.Boolean	'b'	1
INT16	java.lang.Short	'q'	2
UINT16	Undefined	Undefined	Undefined
INT32	java.lang.Integer	'i'	4
UINT32	Undefined	Undefined	Undefined
INT64	java.lang.Long	't'	8
UINT64	Undefined	Undefined	Undefined
DOUBLE	java.lang.Double	'd'	8
STRING	java.lang.String	's'	NULL terminated
OBJECT_PATH	Undefined	Undefined	Undefined
SIGNATURE	Undefined	Undefined	Undefined
ARRAY	Undefined	Undefined	Undefined
STRUCT	Undefined	Undefined	Undefined
VARIANT	Undefined	Undefined	Undefined
DICT	Undefined	Undefined	Undefined
UNIX_FD	Undefined	Undefined	Undefined

Table 10: Argument types

The second message related to d-bus remote procedure calls is the response. This is a marshaled d-bus message as described above.
All d-bus RPC request are handled in a synchronous way. The next RPC request will not be handled until the response is send (or only the preliminary response in case of error). Asynchronous SHOULD be possible if Android request multiple D-bus RPC services.
Any d-bus responses may not exceed 4000 bytes. The accessory MUST send a d-bus error instead of . The error type must be
Error type	Error type description
nl.ict.aab.dbus.messageTooLong	If the RPC call is too long.

### D-bus signal
The D-bus signal stream is unidirectional (from accessory to android). At the start, Android should give the following arguments in a open request when opening the stream:
Offset	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	1 - Destination port					Length of data
4	32	'O'					3 - Requested protocol					Arguments length 0-4000
8	64	D-bus signal arguments [Variable size elements See Error: Reference source not found]

Table 11: Request for d-bus signals
Field	Specification
Busname	NULL terminated string, a empty string is allowed
Object path	NULL terminated string, a empty string is allowed
Interface	NULL terminated string, a empty string is allowed
signalName	NULL terminated string, a empty string is allowed

Table 12: D-bus signal arguments
The combined size for the D-bus signal arguments MUST NOT exceed 3000 bytes, as is specified in Table 3: Port open request message. Passing NULL for all values SHOULD not be done, as you will receive all d-bus signals. All d-bus messages matching the arguments will be send from the accessory to the android device. This is send in the marshaled message format as described in chapter D-bus.
#### Example
Android → Accessory
A Port open request message to the service spawner for d-bus signals. The service identifier is 0x03 and the arguments are:
nl.ict.sensors (NULL)
/nl/ict/sensors (NULL)
nl.ict.sensors (NULL)
(NULL)

0x010031006F032F006E6C2E6963742E73656E736F7273002F6E6C2F6963742F73656E736F7273006E6C2E6963742E73656E736F72730000

Android ← Accessory
The accessory send a port Port open status message back and assigns port 8 to the requested service.

0x010008007308000100000000

Android ← Accessory

The signal service does not need any more information from the Android device to operate, so it closes the input stream from the Android device.

0X000008007308000400000000

Android ← Accessory
Some time later, a signal might be send from the accessory. This includes a d-bus marshaled message.

0x0800AA006C0401010A000000020000008D00000001016F00150000002F6F72672F667265656465736B746F702F4442757300000002017300140000006F72672E667265656465736B746F702E4442757300000000030173000C0000004E616D6541637175697265640000000006017300050000003A312E3931000000080167000173000007017300140000006F72672E667265656465736B746F702E4442757300000000050000003A312E393100

Please note: The marshaled message is received as a whole here, but this is not guaranteed. Message will be segmented if they are bigger then the allowed data size as specified in the Multiplexed message. Messages who are smaller might be segmented.

Android → Accessory
Signals will be send to the Android device until the Android device closes the port:

0x0000AA007308000400000000